## Slide 1: Machine Learning Problems in Cryo-EM
Hanlin Gu, HKUST
2018-11-21

## Slide 2: Outline
Introduction for cryo-em
Particle picking problem
Denoising problem
Clustering problem

## Slide 3: Experimental techniques to resolve atomic structure
https://www.creative-biostructure.com/comparison-of-crystallography-nmr-and-em_6.html

## Slide 4: Cryo-EM: Rising star
1974: birth
2012: Resolution Revolution
2017: Nobel Prize

## Slide 5: Cryo-EM
Cryo-electron microscopy (cryo-EM), or electron cryomicroscopy, is a form of transmission electron microscopy (TEM) where the sample is studied at cryogenic temperatures (generally liquid nitrogen temperatures ~ 80K).

## Slide 6: Cryo-EM: ”Take photo” of biomolecular
Rafael Fernandez-Leiro and Sjores H.W.Scheres, Nature, 537(7620), 339-346 (2016)
Structural reconstruction from the micrograph

## Slide 7
Photos: Projection of a molecular along a certain direction
Distorted by the non-ideal lens and noises from multiple sources

## Slide 8: Experiments vs. Structural Reconstruction
Assign correct angle for each noisy image

## Slide 9: Projection slice theorem
Once we have the correct angles, we can put the slices back and then get the structure
Molecular Cell 58, May 21, 2015

## Slide 10: Common protocol

## Slide 11: Popular software: cryoSPARC
Maximized posterior probability
  Stochastic gradient descend
﻿NATURE METHODS | ADVANCE ONLINE PUBLICATION | 1

## Slide 12: Outline
Introduction for cryo-em
Particle picking problem
Denoising problem
Clustering problem

## Slide 13: Problem 1: Particle picking
Selection of a tremendous number of (e.g., hundreds of
thousands of) high-quality particles from
micrographs.
This particle picking step is a labor-intensive step,
In the past, particles from cryo-EM micrographs are often
selected manually.

## Slide 14: Fully automated particle picking
https://arxiv.org/pdf/1605.01838.pdf

## Slide 15: Steps:
Scoring: a sliding window scans micrograph as input data. Getting a score map by cnn.
Cleaning: Remove the pixel point which neighbors(include itself) are all larger than a cutoff.
Filtering: Refine the current set of particle candidates and also identify the center coordinates of the final remaining particles from the scored map.
Sorting: Sort the remaining particle candidates according to their prediction scores.
Iteration：Using the particles picked by the previous CNN classifier which was trained over the known particles of other molecules to further refine the CNN model.

## Slide 16: Evaluate
Evaluated the performance of our particle picking approach mainly by comparing the automated picking results to the corresponding reference particles picked manually by human experts

## Slide 17: Outline
Introduction for cryo-em
Particle picking problem
Denoising problem
Clustering problem

## Slide 18: Noise in cryoEM images would obscure the structural differences
Very large noise and unregular
noise
When noise level is comparable with differences between conformations, it is hard to discriminate conformations
Apo ribosome, K2 detector
Simulated images at SNR=0.1, MSE(X1,X2)=11, var(noise)=39
MSE=0.029
MSE=0.026
Inter-class diffe ~ intra-class diff

## Slide 19: Benefits of denoising
Denoising cryoEM images can
  Benefit angular classification
  Better distinguish different conformations
  Others: improve the performances of common-line detection, improve resolution of reconstructed 3D maps
Far East J Appl Math. 2010 Aug; 45(2): 83–161.

## Slide 20: Denoising can benefit discriminating conformations
MSE=0.029
MSE=0.026
MSE=0.0046
MSE=0.005
Before denoising
After denoising
Denoising algorithm: kSVD

## Slide 21: Existing methods in softwares
Existing methods in softwares and challenges
  Relion, CryoSPARC: Gaussian noise model, denoising is coupled with the classification process:
    Very time consuming and cost a lot of memory
  Aspire: Covariance Wiener Filtering (CWF) (Singer, et al.) needs large number of samples in order to have a good denoising performance.
    CWF is computational intensive, and not work well with small data samples.
    Ensemble method, memory cost is very high
,
Notes: Source of noise: ice
Why low snr? Low dose, since the electron beam would benefit the electron density of molecule, each sample is only used once

## Slide 22: Some other traditional methods
Traditional Wiener Filter
Total variation method: chambolle
Nonlinear local
Mean, median..
http://scikit-image.org/docs/dev/api/skimage.restoration.html
Notes: Source of noise: ice
Why low snr? Low dose, since the electron beam would benefit the electron density of molecule, each sample is only used once

## Slide 23: Some cutting edge methods in applied mathematics
K-SVD
Data-Driven Tight Frame for Multi-Channel Images: DDTF
Block-matching and 3D filtering: BM3D
Notes: Source of noise: ice
Why low snr? Low dose, since the electron beam would benefit the electron density of molecule, each sample is only used once

## Slide 24: Block-matching and 3D filtering
Finding the image patches similar to a given image patch and grouping them in a 3D block
3D linear transform of the 3D block and set threshold to remove high frequency data;
inverse 3D transformation
Aggregation: average images of block in different weights
https://www.cs.tut.fi/~foi/GCF-BM3D/BM3D_TIP_2007.pdf

## Slide 25: K-SVD
In applied mathematics, K-SVD is a dictionary learning algorithm for creating a dictionary for sparse representations, via a singular value decomposition approach.
K-SVD is a generalization of the k-means clustering method, and it works by iteratively alternating between sparse coding the input data based on the current dictionary, and updating the atoms in the dictionary to better fit the data.
Wikipedia: K-SVD
IEEE TRANSACTIONS ON SIGNAL PROCESSING, VOL. 54, NO. 11, NOVEMBER 2006

## Slide 26: K-SVD
https://sites.fas.harvard.edu/~cs278/papers/ksvd.pdf

## Slide 27: Algorithm proposed: Data Driven Tight Frame (DDTF)
https://www.sciencedirect.com/science/article/pii/S1063520313000924

## Slide 28: Comparison of the cutting edge algorithms in denoising simulation data
c.f. Clean image
SNR 0.8
SNR 0.4
DDTF
BM3D
KSVD

## Slide 29
SNR 0.2
Output
SNR 0.1
DDTF
BM3D
KSVD
c.f. Clean image

## Slide 30
SNR 0.05
Output
SNR 0.01
DDTF
BM3D
KSVD
c.f. Clean image

## Slide 31: Performances of CWF in aspire
Covariance Wiener filtering achieves the denoising of an image by Wiener filtering, where the statistical quantities (mean, covariance matrix) are estimated from massive noisy images.
Fast since steerable PCA is applied to reduce the dimensionality
Achieve better performances when the number of noisy images increases.
https://arxiv.org/abs/1602.06632

## Slide 32: Performances of CWF vs. # of images
Clean images
SNR=0.01
Denoised results using 1000 images
Cost 2.5G memory
Denoised results using 100 images
Synthetic dataset using P.falciparum 80S ribosome bound to E-tRNA

## Slide 33: Performance of CWF vs. SNR
SNR=0.8
SNR=0.4
SNR=0.1
SNR=0.05
Using 2000 images to denoise

## Slide 34
Chart: Comparison of Mean square error of denoised images relative to the clean images
| SNR=0.8 | SNR=0.4 | SNR=0.2 | SNR=0.1 | SNR=0.05
DDTF | 0.0036 | 0.0093 | 0.0093 | 0.0239 | 0.0587
CWF | 0.0504 | 0.0134 | 0.0174 | 0.0198 | 0.0242
BM3D | 0.0241 | 0.0621 | 0.0655 | 0.1736 | 0.1532
KSVD | 0.0352 | 0.0534 | 0.1094 | 0.1615 | 0.1591

## Slide 35
Chart: Comparison of PSNR of denoised images
| SNR=0.8 | SNR=0.4 | SNR=0.2 | SNR=0.1 | SNR=0.05
DDTF | 48.5024 | 44.3806 | 44.3806 | 40.2814 | 36.379
CWF | 37.0411 | 42.7944 | 41.6599 | 41.0987 | 40.2272
BM3D | 40.2452 | 36.1345 | 35.903 | 31.6699 | 32.2128
KSVD | 38.6 | 36.1345 | 35.903 | 31.6699 | 32.2128
The result is bad as the SNR is low

## Slide 36: Dataset
1. Choose the first 10000 evidence clean images which from cryosparc.
Sometimes, it is necessary to add contrast transfer function to clean images as reference.
Noisy image = clean image* CTF (in fourier domain)+ noise
Blurring

## Slide 37: GAN_structure
https://www.biorxiv.org/content/biorxiv/early/2018/02/12/256792.full.pdf

## Slide 38: GAN_structure

## Slide 39: Loss function
The g loss and d loss are gradually stable

## Slide 40: One criterion: MSE between denoised image and clean image
 | CTF | Non CTF
MSE(test for 500 , train for 9500) | 0.0103 | 0.0046

## Slide 41: Result(no ctf):
But the right picture is a little blur, maybe you take some improvements.

## Slide 42: Reason for blurring
Deconvolution overlap cause the blur of image

## Slide 43: Method
A kernel size that is divided by your stride, avoiding the overlap issue.

## Slide 44: Other criterion:
Using software such as cryosparc or relion to reconstruct.
（https://cryosparc.com/docs/tutorials/t20s/）
Using kam theory to reconstruct.
（https://www.ncbi.nlm.nih.gov/pmc/articles/PMC4678003/）
The less the resolution you get, the more accurate result you derive.

## Slide 45: The structure after 600 iteration(using cryosparc)

## Slide 46: Discussion
Other improvements? Design you own network structure.
Other than GAN, using autoencoder or VAE to denoise the experimental data
Using the multiple images denoising methods taking using of the connections of images.

## Slide 47: Outline
Introduction for cryo-em
Particle picking problem
Denoising problem
Clustering problem

## Slide 48: Problem 3 :Clustering conformations
str1
str5
-153
-149
-144
-140
-136
Close Open
Goals: Classify the five conformations that are within same projection angle
Choosing ~2000 images from north pole for analysis including 5 equal conformation

## Slide 49: Difficulties
With the increasing of conformations, the difference between conformations is less and less.
Because the images are in 2D different angles, how to find a rotational invariant variable becomes a difficulty.
The noise in image will influence the clustering result seriously.

## Slide 50: Two-stage Classification of Cryo-EM images
1st ACF classification stage
  Fast enough to remove the majority of images (>80%) in full space that are far away from basis set angle efficiently
  With space angle error and mis-assignment error during this stage
2nd classification by enhanced basis set stage
  Brute force classification of image by pixel information to void space angle error
  Remove outliers to obtain the final results
  Accurately get the proportion distribution by reducing mis-assignment error

## Slide 51: Result
The brute force classification method is better than ACF method, it can

## Slide 52: EMBEDDING(ACF function)
There are 3 close conformations which are hard to discriminate.

## Slide 53: Discussion
Other clustering methods?
When adding the noise in the images, is it clustering well after denoising?

## Slide 54
Thank you!